承  认   书

## SPECIFCATION

|  | 客 户 资 料 CUSTOMER’S INFORMATION |
| --- | --- |
| 产品名称：LED灯 PRODUCTION NAME: | CUSTOMER: |
| 产品型号: 8MM-RGBW-A PRODCTION TYPE: | 机型: MODEL NO: |
| 规格摘要: TYPE:8MM－共阴雾状红翠蓝 | 料号: PART NO: |

确认后请回传PLEASE  RETURN  BY  ONE COPY

| 日期:2014-05-20 DATE: | 承办人: ISSUEDER: |
| --- | --- |
| 客户确认 APPROVED BY |
| 签名: 日期: SIGN: DATE: |
| 结论 RESULT： |

深圳市光越光电子有限公司

电话(TEL):0755-83033461      传真(FAX):0755-83930117

发货地址:广东省深圳市福田区华强花园

设计(DESIGN):            检查(CHECKED):              批准(APPROVED):

# Text boxes

- Feature

- Two dhips are matched for unifom

- llight output, wide viewing angle

- indication, mounted

- on edge of card

- Multi-colour

- permutations

- available

Package Dimension:

| Part No. | Polar | Lens Color | Source Color |
| --- | --- | --- | --- |
| 8MM-RGBW-A |  | Diffused | Red Green Blue |
|  | cathode |  |  |

Notes:

- All dimensions are in millimeters.

- Tolerance is ±0.25mm unless otherwise noted.

- Protruded resin under flange is 1.0mm max.

Approved By：               Designed By：魏青华

Absolute Maximum Ratings at Ta=25℃

| Parameter | MAX | Unit |
| --- | --- | --- |
| Power Dissipation | R | 120 | mW |
| Peak Forward Current (1/10 Duty Cycle,0.1ms Pulse Width) | R | 100 | mA |
| Continuous Forward Current | R | 20 | mA |
| Operating Temperature Range | -25℃ to +85℃ |
| Storage Temperature Range | -25℃ to +85℃ |
| Lead Soldering Temperature (4mm From Body) | 260℃ for 5 seconds |

Electrical Optical Characteristics at Ta=25℃

| Parameter | Symbol |  | Min. | Typ. | Max. | Unit | Test Condition |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Luminous Intensity | Iv | R | 300 | 400 | ---- | mcd | IF=20mA(Note 1) |
|  |  | G | 1000 | 1200 | ---- |  |  |
|  |  | B | 600 | 800 | ---- |  |  |
| Viewing Angle | 2θ1/2 |  | ---- | 60 | ---- | Deg | (Note 2) |
| Peak Emission Wavelength | λp | R | 620 | 623 | 625 | nm | IF=20mA |
|  |  | G | 520 | 525 | 530 |  |  |
|  |  | B | 460 | 465 | 570 |  |  |
| Spectral Line Half-Width | Δλ |  | ---- | 30 | ---- | nm | IF=20mA |
| Forward Voltage | VF |  | R:2.0 | Y:2.0 | G:2.0 | V | IF=20mA |
| Reverse Current | IR |  | ---- | ---- | 10 | μA | VR=5V |

Note:

- Luminous intensity is measured with a light sensor and filter combination that approximates the CIE eye-response curve.

2. θ1/2 is the off-axis angle at which the luminous intensity is half the axial luminous intensity.