ATTEN AT9205D Digital Multimeter

AT9205D is easy to operate ,accuracy ,compact, rugged, battery operated, handheld 3½ digital multi-meter for measuring DC and AC voltage, DC and AC current, Resistance and Diode, Capacitor, Transistor(hFE), Continuity Test and  Temperature or frequency. The Dual slope A-D Converter uses C-MOS technology for auto-zeroing, polarity selection and over-range indication. It also has full overload protection.

AT9205D is an ideal instrument for use in the field, laboratory, workshop, Industrial maintenance, DIYers and home applications.  Key Features.

• All ranges fully protected and full overload protection

• Single 30 position easy to use rotary switch for FUNCTION and RANGE selection.

• High sensitivity of 100µV

• Automatic over range indication

• Auto power-off

• Dual slope A-D Converter uses C-MOS technology.

• Auto zero and auto polarity selection

• Over range indication

• Continuity test with LED indication and buzzer indication

Technical Specifications

Function  Range   Accuracy  Resolution

DC Voltage  200mV/2V/20V/200V/1000V  ± (0.5% +2)  100µV – 5V

AC Voltage  200mV/2V/20V/200V/750V   ± (1.0% +2)  100µV – 1V

DC Current  20uA/2mA/20mA/200mA/20A  ± (1.0% +2)  1µA – 10mA

AC Current  20uA/2mA/20mA/200mA/20A  ± (1.5% +5)  1µA – 10mA

Resistance  200Ω/2K/20K/200K/2M/200M   ± (1.0% +2)  0.1 ohm – 100K ohm

Capacitance  20nF/200nF/2uF/20uF/200uF   ± (3.0% +2)  1PF – 10nF

Frequency Test  200KHz  ± 1% of  rdg + 1 digit  100Hz

Diode Test  Yes, Approx forward voltage

Transistor Test  Yes, Approximate hFE value

Continuity Test  Yes, Buzzer sounds

Automatic Power off  Yes, keeping idle for about 15min.

General Specifications

Maximum Display  1999 counts (3 ½ digits) with automatic polarity indication and eng. Unit

Indication Method  LCD Display

Measuring Method  Dual –Slope integration A-D converter system

Overrange indication  “1” Figure only on the display

Maximum common mode voltage  500V DC/AC rms

Reading rate  2-3 reading per sec (approx.)

Temperature

Operating:10°C to + 40°C, 32°F to 104°F,

Not operating: -10°C to +50°C, 14°F to 122°F

Power supply  One 9V battery (NEDA 1062 6F22 type or equivalent)

Low Battery indication   to the left of display Size   88 x 170 x 38 mm

Weight  340g

Standard Accessories  Test leads, Operating Manual

Qty/Ctn  60

Size of Shipping Package   50 x 40 x 40cm

Gross weight of Shipping Package   21Kg

An ISO-9001Certified Manufacturer

ATTEN ELECTRONICS CO., LTD.

Building A29, Tanglang Industrial Zone, Xili

Nanshan, Shenzhen 518055

P.R.China

Tel.: +86-755-86021376,  Fax:  +86-755-61618291

Sales: atten@atten.com.cn

Marketing : atten8@atten.com.cn